## Slide 1: Analog VLSI Circuit Final Project
Presented By-
Group-4
Akash Ganguly – SC18B072
Kothadiya Prince - SC18B078
Kshitij Singh – SC18B079
Aditya Amrit – SC18B087
Vivek Garg – SC18B093
Notes: Good Morning Sir, Sir, we Group – 4 will be presenting on fully differential Opamp with rail-to-rail input with CMFB. The members of our group are Akash, Prince, Aditya, Vivek and myself Kshitij
Moving on to Contents or overview what we will be discussing is:

## Slide 2: Contents
Objective
  Design Requirement
Current Mirror Network
  Cascode pair biasing
Folded Cascode Design
  Design Calculation
  NMOS-PMOS-Overall Design
  Results
CMFB
  Design
  Buffer Design
  Results & Analysis
2nd Stage Design
  Design Calculation
  Results
Final Results & Conclusion
References
Notes: Here, We have

## Slide 3: Objective

## Slide 4: Design Requirements
Fully Differential OpAmp
Rail-to-Rail input capability
CMFB
Notes: Gaim more than 70dB

## Slide 5: Current Mirror

## Slide 6: Current Mirror
Notes: Using 10 micro amplere current source
4 Legs –M1, M11M2, M12,13,14 , M20,15,19
Source se transistor ko bias kr rhe hai...
NMOS The tail current sourcess... ye bias kr rhe hai
M1 and current se koi bhi bias kr skte
M11 se Vtp Bias kr rhe
M13,14 se koi bhi cascode ko bias kr skte Vb2 ko bias kiya Vb1
M15,20 cascode ke upar wale pmos ko bias kr rhe Vb3,4
Vtp – pmos ka tail current course.. M11 (size-2) ka replicate krega.. At M0p (size-27)..so 13.5 times zada current..
Vtn – nmos ka tail current – M1 ka current replicate krega.. At M0n (size-32) so 16 times zada and also bias nmos tail current 2nd stage, CMFB and buffer
Vb1 - replicate current from M14, at M3 M4 (size-27) so 13.5 times zada current..
Vb2 - replicate current from M13, at M5 M6 (size-15) so 7.5 times zada current..
Vb3 - replicate current from M15(size-4), at M7 M8 (size-31) so 7.75 times zada current..
Vb4 - replicate current from M20(size-4), at M9 M10 (size-62) so 15.5 times zada current..

## Slide 7: Current Mirror
Vtp – biases PMOS Tail Current for M0p Transistor
Vtn – biases NMOS Tail Current for M0n Transistor and others
Vb1 – biases M3 and M4 Transistor( Lower NMOS Stack)
Vb2 – biases M5 and M6 Transistor(Upper NMOS Stack)
Vb3 – biases M7 and M8 Transistor(Lower PMOS Stack)
Vb4 – biases M9 and M10 Transistor(Upper PMOS Stack)
Notes: Vtp – pmos ka tail current course.. M11 (size-2) ka replicate krega.. At M0p (size-27)..so 13.5 times zada current..
Vtn – nmos ka tail current – M1 ka current replicate krega.. At M0n (size-32) so 16 times zada and also bias nmos tail current 2nd stage, CMFB and buffer
Vb1 - replicate current from M14, at M3 M4 (size-27) so 13.5 times zada current..
Vb2 - replicate current from M13, at M5 M6 (size-15) so 7.5 times zada current..
Vb3 - replicate current from M15(size-4), at M7 M8 (size-31) so 7.75 times zada current..
Vb4 - replicate current from M20(size-4), at M9 M10 (size-62) so 15.5 times zada current..

## Slide 8: Current Mirror
Notes: 4 Legs –M1, M11M2, M12,13,14 , M20,15,19
Source se transistor ko bias kr rhe hai...
NMOS The tail current sourcess... ye bias kr rhe hai
M1 and current se koi bhi bias kr skte
M11 se Vtp Bias kr rhe
M13,14 se koi bhi cascode ko bias kr skte Vb2 ko bias kiya Vb1
M15,20 cascode ke upar wale pmos ko bias kr rhe Vb3,4
Vtp – pmos ka tail current course.. M11 (size-2) ka replicate krega.. At M0p (size-27)..so 13.5 times zada current..
Vtn – nmos ka tail current – M1 ka current replicate krega.. At M0n (size-32) so 16 times zada and also bias nmos tail current 2nd stage, CMFB and buffer
Vb1 - replicate current from M14, at M3 M4 (size-27) so 13.5 times zada current..
Vb2 - replicate current from M13, at M5 M6 (size-15) so 7.5 times zada current..
Vb3 - replicate current from M15(size-4), at M7 M8 (size-31) so 7.75 times zada current..
Vb4 - replicate current from M20(size-4), at M9 M10 (size-62) so 15.5 times zada current..
R -> 200 to 300 mv drop approx. to Vth drop because we are using a low voltage cascode bias circuit

## Slide 9: Folded Cascode Rail-to-Rail Design

## Slide 10: Design Budgeting
Let’s choose gm=1 mS
Let the design Vin,cm=0.9V
0.6V – Vgs biasing
0.3V – Vdssat + margin for tail current source

## Slide 11: NMOS Characterization
Id: 1.13e-05
Vgs: 6.00e-01
Vds: 3.00e-01
Vbs: 0.00e+00
Vth: 4.82e-01
Vdsat: 1.30e-01
Gm: 1.34e-04
We must scale NMOS such that gm=1mS
Wreq.d=7.4*W1

## Slide 12: PMOS Characterization
Id: 1.62e-06
Vgs: 6.00e-01
Vds: 3.00e-01
Vbs: 0.00e+00
Vth: 5.16e-01
Vdsat: 9.91e-02
Gm: 2.35e-05
We must scale PMOS such that gm=1mS
Wreqd=42.5*W1

## Slide 13: NMOS Input Pair
Name: m1n m2n
Model: n18 n18
Id: 7.39e-05 7.39e-05
Vgs: 6.17e-01 6.17e-01
Vds: 1.27e+00 1.27e+00
Vbs: -2.83e-01 -2.83e-01
Vth: 5.30e-01 5.30e-01
Vdsat: 1.12e-01 1.12e-01
Gm: 9.75e-04 9.75e-04
Gds: 1.99e-05 1.99e-05
m0n
n18
1.48e-04
5.93e-01
2.83e-01
0.00e+00
4.63e-01
1.42e-01
1.69e-03
5.83e-05

## Slide 14: PMOS Input Pair
Name: m1p m2p
Model: p18 p18
Id: -6.30e-05 -6.30e-05
Vgs: -6.47e-01 -6.47e-01
Vds: -1.30e+00 -1.30e+00
Vbs: 2.53e-01 2.53e-01
Vth: -5.30e-01 -5.86e-01
Vdsat: -9.10e-02 -9.10e-02
Gm: 9.77e-04 9.77e-04
Gds: 1.67e-05 1.67e-05
m0p
p18
-1.26e-04
-7.17e-01
-2.53e-01
0.00e+00
-4.32e-01
-2.42e-01
7.37e-04
1.06e-04

## Slide 15: Main Transistor Stack

## Slide 16: Main Transistor Stack
 | M3 | M5 | M7 | M9
ID | 149μA | 86.1μA | 86.1μA | 160μA
VGS | 601mV | 637mV | 759mV | 700mV
gm | 1.75mS | 1.05mS | 0.841mS | 1.49mS
ro | 10.2kΩ | 27.78kΩ | 56.82kΩ | 13.26kΩ

## Slide 17: Circuit Design
NMOS-PMOS Folded Cascode design

## Slide 18: DC Analysis
Input CM Voltage
  Sweep from -0.5V to 2.5V
Output DC Voltage
  Range: 0.7V to 1V
Rail to Rail working capability
  Input CM voltage
  0.7V to 1V
Notes: Enough Headroom in mid-range
Low headroom in upper and bottom range

## Slide 19: AC Analysis(Vcm=0.9V)
Notes: ~50 dB gain, 564 MHz – UGF, PM- >80 (because 1st stage only)

## Slide 20: AC Analysis
Notes: Working for input common mode voltage of 0.9 V
Low gain for other case of input -> not working rail to rail

## Slide 21: CMFB

## Slide 22: Principle of CMFB
Common Mode Feedback to correct for Vcm because of variation in PMOS and NMOS current pairs
Compare the Common mode voltage to reference voltage
Output signal of CMFB Stage can be fed back
Providing it on gate terminal helps in controlling Vgs and hence, current through it.

## Slide 23: Detection of Common mode voltage
Sensed by simple resistor
But direct resistor comes parallel to Rout
Results in low gain
Require high value of Resistor
Solution is to use buffer stage
Followed by low value resistor to detect the output VCM

## Slide 24: Source Follower
Benefits:
Very high input impedance
Price:
Voltage(VGS ) drop across the M2 transistor
Reference voltage = VCMref- VGS
VCMref = 0.9V
VGS = 0.593V ≈ 0.6V
Notes: High input impedance -> Rout won’t be affected

## Slide 25: Correction for Common Mode voltage
Common Mode voltage detected
CMFB stage: 5T OTA
Output: Vo_5T
Reference voltage : (V-)
  (V-) = VCMref – VGS = 0.3
Notes: Now after the deduction of Vcm now we need to compensate for current difference, in this project, it is done by correcting nmos gate value. Here as you can see the voltage V- is used to be 0.3v as a reference source because of voltage drop across the buffer. Later we would see the variation in voltage

## Slide 26: DC Analysis
Input CM Voltage
  Sweep from -0.5V to 2.5V
Output DC Voltage
  Not much Variation.
Rail to Rail working capability
  Input CM voltage
  Full Range
Notes: After the addition of CMFB, we can see the output Common Mode voltage is improved drastically with a approx. voltage level of 900mv, this provide much more headroom for signal swing which was missing in the previous stage.

## Slide 27: DC Analysis
Input CM Voltage
  Sweep from -0.5V to 2.5V
Output CM Voltage
  Range: 0.4V to 1.4V
Output of CMFB Stage
  Range: 0.4V to 1.4V
  Similar behavior
Notes: Here we can see the variation in input to the 5T OTA with the Vcm sweep and similarly output of OTA, Here we can see the input to OTA is around 270mv because of the deduction of Vgm voltage from buffer stage

## Slide 28: AC Analysis
Folded cascode with CMFB
Notes: Now we can see the gain is much improved from the previous stage which had very less gain for values under 0.4 and 1v but still less than the required gain
Here we can see the gain is in the range of 50 db

## Slide 29: Transient Analysis
To simulate current disturbance: extra current source used.
Current sources in parallel with the MOSFET
Current source: Pulse input
Notes: Here we used an extra current source element to simulate for sudden change in current due to environmental factors.
we can see the current sources in parallel with the PMOS
Hence this will simulate for change in current level for NMOS and PMOS pairs
Now CMFB has to compensate for this change by correcting the NMOS current value, we would first see the transient analysis then proceed to voltage compensation

## Slide 30: Results
Ts = 0.4µS
Notes: Here we can see, first the transient analysis of the signal. The signal is almost perfect for complete duration of pulse and have a very small disturbance near the transition stage, this settling time was measured to be 0.4 us

## Slide 31: Transient Voltage analysis
Ts = 0.4µS
Notes: Now here we can see, as the current depicted in green graph drops, the value of the 5T OTA also drops, this is because as the parallel current source to pmos simulates for extra current in pmos pair than of nmos pair, and hence when the current source turns off, so pmos current also decrease hence now CMFB need to make sure the nmos current also need to be decreased, which is being done here as seen in the red graph, correspondingly we can see the change in the common mode voltage i.e, V+ is very less although we can see a disturbance in the signal, this disturbance is restricted to 0.4us only.

## Slide 32: 2nd Stage
Notes: Moving on to next part that is the 2nd stage. As we have seen earlier that the gain of 1st stage with CMFB is in the range of around 48db to 50dB

## Slide 33: Design Budgeting
Common source amplifier
Design parameters:
  Vgs(for second stage)
    Vgs = VDD-VCMRef = 1.8V-0.9V = 0.9V
  Av,req(Required gain) = 17.78
Calculation:
  Av,req= 17.78 = gm* Rout
  (2.22m) * (8kΩ) = 17.78
  Rout 8kΩ
Notes: So we have implemented common source amp for this stage. Vgs for this was calculated and was found to be around 0.9V. And we designed it to give a gain of 25dB
Which is 17.78 in absolute value. We divided this gain in two parts 8k and 2.22m and took Rout to be 8k and gm to be 2.22ms.

## Slide 34: PMOS Characterization
Scaling factor(multipliers) = = 36.98 37
Notes: Now comes the PMOS characterization. We can see from the plot that at 0.9V, gm is around 60us and requires is 2.22ms so we get the scaling factor as 37.

## Slide 35: 2nd Stage Design
2nd Stage Circuit
Operating Point
Notes: then we implemented the CS Amp using scaled transistor here we can see that M25 is our main transistor and M26 is providing the required current required current to M25 using the current mirror explained by kshitij. This is the noperating point of the 2nd stage

## Slide 36: Simulation Results
Gain Plot
gm = 2.04mS
Rout = 10.672kΩ
Gain(Av) = 23.32dB
Cut-off Frequency(fc)
  = 29.83MHz
Notes: So now this is the simulation result for this stage. This is the AC gain plot of the 2nd stage and we can see that we got gm to be 2.04mS and Rout and Av and Cut off freq

## Slide 37: Phase Compensation(Miller compensation)
Resistor Calculation:
  Rz
  = 490.196Ω
  Taking Rz=500Ω
Taking arbitrary value for capacitor cc = 500fF
Notes: The phase margin that we were getting for both the stages and CMFB combined came out to be –ve so we have used the miller compensation for the phase compensation. It is basically adding capacitor between the Input and output of 2nd shifting the dominant pole(ie 1st stage) to right hand side improving the GM but at the same time it also introduces a zero in RHP which overall deteriorates our overall phase margin so we add a resistor almost equal to 1/gm and greater then that. So we took rz as 500 and took a arbitrary value of c as 500fF

## Slide 38: Circuit Design
2nd Stage with miller compensation(between 1st and 2nd stage)
Notes: Here we can see the circuit design which is basically adding this R and C

## Slide 39: Simulation result
With Miller Compensation
Without Miller Compensation
Gain Cross-over frequency = 1.584GHz
Phase margin = -201.48+180 = -21.48(Unstable)
Gain Cross-over frequency = 263.02 MHz
Phase margin = -117.81+180 = 62.19(stable)
Notes: Now this is sim results phase margin was -21.48 that means the system is unstable(oscillations) after compensation we got pm of 61.2 which is very good and we can see that UGF is 263MHz which satisfies our design requirement of UGF >100MHz

## Slide 40: Results

## Slide 41: DC Analysis
Input CM Voltage
  Sweep from -0.5V to 2.5V
Output DC Voltage of Stage-1
  Range: 0.4V to 1.4V
  Not much variation
Output DC Voltage of Stage-2 (Final O/P)
  Range: 0.4V to 1.4V
  Not much variation
Rail to Rail working capability
  Input CM voltage – Full Range
Notes: Enough Headroom in mid-range as well as low and high range

## Slide 42: AC Analysis (VCM = 0.9V)
Notes: 76 dB gain, 436 MHz, PM - 48

## Slide 43: AC Analysis (VCM sweep)
Notes: Input CM sweep – 0 to 1.8 V
gain- not much change
Only 2-3 case – slightly less than 70 dB but it’s good.
We can say it is working in full rail-to-rail input range

## Slide 44: AC Analysis (VCM sweep)
Notes: Then we increase the input CM range..
-0.5V to 2.5V
Working fine for all the cases except last 3 cases..

## Slide 45: Results & Conclusion
Gain
  65.3 dB to 76.63 dB
BW
  156.055 kHz to 77.16 kHz
UGF
  263 MHz to 436.5 MHz
  UGF > 100 MHz
Phase margin
  48 to 63
Power Consumption (Overall)
  1.8*1.37m = 2.467mW
Power Consumption (w/o bias)
  1.8*1.33m = 2.39mW
Input common mode range
  Rail-to-Rail
CMFB
  Working

## Slide 46: Improvements
Rail-to-Rail input capabilities in stage-1 (folded cascode)
Gm Calibration
Overall Gain Improvements

## Slide 47: References
Design of Analog CMOS Integrated Circuits, B. Razavi
ECEN474/704: (Analog) VLSI Circuit Design (Spring 2018), Sam Palermo Analog & Mixed-Signal Center, Texas A&M University
  Lecture 15: Fully Differential Amplifiers & CMFB
  Lecture 17: Fully Differential Amplifiers & CMFB
Lecture notes

## Slide 48: THANK YOU!